SECTION 23 34 33

AIR CURTAINS

This specification includes Mars Air Systems Low Profile Series 2 air curtains for environmental control, flying insect control, and temperature control. Heating options are available for the LPV2 series for electric, hot water, and steam.

Low Profile Series 2 air curtains are available for openings 25 inches to 144 inches wide and come in two varieties: the LPV2 series for invironmental and flying insect control, and the LPN2 series for flying insect control (ETL Sanitation). Recommended installation heights for the LPV2 series are up to 8 feet for environmental separation and temperature control applications and up to 7 feet for flying insect control applications. Recommended installation height for the LPN2 series is 7 feet for flying insect control (ETL Sanitation). Countertop and/or concessions stand installations require intake filters. Low Profile Series 2 air curtains are typically effective to resist wind loads up to 9 mph for temperature control applications. Note that velocities specified for each unit are based on a 60 Hz power source.

Typical installations include commercial, office and retail entrances. Air curtains help reduce heating and cooling costs while expediting the flow of traffic from one work area to another or in and out of a building. At the same time, air curtains can minimize the entrance of windborne dust, fumes, pollutants, and flying insects.

Mars Air Curtain products meet the requirements of all North American and European Union Codes and Standards. For a complete selection guide and assistance with your air curtain configuration, please visit www.marsair.com.

Important Note: This specification contains hidden text appearing in red. To show or remove hidden text in MSWord, click the “File” tab or “Office” icon on the top-left corner, select “Options,” select “Display,” and check or uncheck the box marked “Hidden Text.”

GENERAL

SECTION INCLUDES

SPECIFIER NOTE – Delete items below not required for project.

Air curtains for pedestrian entrances.

Air curtains for countertop and drive through windows.

RELATED SECTIONS

SPECIFIER NOTE – Delete any sections below not relevant to this project; add others as required.

Section 05 50 00 – Metal Fabrications: Concealed steel support members.

Section 06 10 00 – Rough Carpentry.

Section 05 41 00 – Structural Metal Studs.

Section 07 62 00 – Sheet metal flashing.

Section 07 92 00 – Joint Sealants.

Section 08 10 00 – Metal Doors and Frames.

Section 08 33 00 – Overhead Coiling Doors.

Section 08 42 00 – Entrance Doors.

Section 22 10 00 – Plumbing Piping:

Section 23 21 00 – Hydronic Piping: Hot water heating piping to units.

Section 23 22 13- Steam and Condensate Piping: Steam heating piping to units.

Section 26 05 00 – Equipment Wiring: Connections to building power distribution.

REFERENCES

SPECIFIER NOTE – Delete items below not required for project.

ASTM A240 / A240M -10 – Standard Specification for Chromium and Chromium and Chromium-Nickel Stainless Steel Plate, Sheet, and Strip for Pressure Vessels and for General Applications.

ASTM A591 / A591M -98 – Standard Specification for Steel Sheet, Electrolytic Zinc-Coated, for Light Coating Weight (Mass) Application (Withdrawn in 2005, replaced by A879/A879M).

ASTM A879 / A879M -06 – Standard Specification for Steel Sheet, Zinc Coated by the Electrolytic Process for Application Requiring Designation of the Coating Mass on Each Surface.

ASTM A653 / A653M -09a – Standard Specification for Steel Sheet, Zinc Coated (Galvanized) or Zinc-Iron Alloy-Coated (Galvannealed) by the Hot-Dip Process.

AHRI 410-2001 – Standard for Forced-Circulation Air-cooling and Air-Heating Coils.

NSF/ANSI 37 – Air Curtains for entranceways in food and food service establishments – ETL Sanitation.

CRN – Canadian Registration Number Coil.

ANSI Z223-NFPA 54 – National Fuel Gas Code/

UL 507 – UL Standard for Safety Electric Fans – Intertek Testing Services Listed for US and Canada

UL 2021 – UL Standard for Fixed and Location-Dedicated Electric Room Heaters – Listed for US and Canada.

NEC – National Electric Code.

SUBMITTALS

Submit under provisions of Section 01 33 00.

Product Data: Manufacturer's data sheets on each product to be used, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Installation methods.

Shop Drawings: Include plans, elevations, sections, and details, indicating dimensions, tolerances, materials, fasteners, hardware, finish, piping, electrical wiring diagrams, options, and accessories.

SPECIFIER NOTE – Delete the following paragraphs if LEED is not applicable. Review design-phase credits available related to tubular unit skylights, including contribution to IEQ Cr 6.1 Controllability of Systems, IEQ Cr 8.1. Daylighting, EA Cr 1 Energy Optimization, and ID Cr 1 Innovation in Design credits. Consult VELUX representative for detailed support data.

LEED Submittals: Provide documentation of how the requirements of Credit will be met:

List of proposed materials with recycled content. Indicate post-consumer recycled content and pre-consumer recycled content for each product having recycled content.

Product data and certification letter indicating percentages by weight of post-consumer and pre-consumer recycled content for products having recycled content.

SPECIFIER NOTE – Delete selection samples if colors have already been selected.

Selection Samples: For each finish product specified, two complete sets of color chips representing manufacturer's full range of available colors and patterns.

Verification Samples: For each finish product specified, two samples, minimum size 6.25 inches (160 mm) square, representing actual product, color, and patterns.

Manufacturer's Certificates: Certify products meet or exceed specified requirements.

Operation and Maintenance Manual: Submit manufacturer's operation and maintenance manual, including operation, maintenance, adjustment, and cleaning instructions, troubleshooting guide, parts list, and electrical wiring diagrams.

QUALITY ASSURANCE

Manufacturer Qualifications: Minimum ten years documented experience producing the products specified in this Section

Installer Qualifications: Minimum five years documented experience installing products specified in this Section

DELIVERY, STORAGE, AND HANDLING

SPECIFIER NOTE – Delete items below not required for project.

Store products in manufacturer's unopened packaging until ready for installation.

Store in a dry, heated storage area until installation of products.

Protect materials and finish from damage during handling and installation.

SEQUENCING

SPECIFIER NOTE – Delete items below not required for project.

Ensure that locating templates and other information required for installation of products of this section are furnished to affected trades in time to prevent interruption of construction progress.

Coordinate the installation of wiring and control switches for air curtains with the openings and the hardware provided for such openings.

Install after doors, walls, ceilings, and other adjacent surfaces are finished and painted.

WARRANTY

SPECIFIER NOTE – Select the applicable warranty from the following paragraphs as required for the unit(s) specified and delete the one not required.

Standard five-year limited parts warranty for unheated units against defects in workmanship and material.

Standard 18-month limited parts warranty for heated units against defects in workmanship and materials.

PRODUCTS

MANUFACTURER

Acceptable Manufacturer: Mars Air Systems, LLC; 14716 South Broadway St., Gardena, CA 90248. Tel: (310) 532-1555 or (800) 421-1266. Fax: (310) 324-3030. Email: info@marsair.com. Web: www.marsair.com.

Delete one of the following two paragraphs: coordinate with requirements of Division 1 section on product options and substitutions.

Requests for substitutions will be considered in accordance with provisions of Section 01 33 00.

SPECIFIER NOTE – Select the type and sizes required and delete those not required. Indicate the door/opening height for each air curtain on the Drawings or on the Schedule at the end of this Section. If more than one type and/or size is required, indicate the location of each on the Drawings or on the Schedule at the end of this Section.

AIR CURTAIN ASSEMBLIES

Motor Fan Assembly: Design for easy removal, assembly, repair, and maintenance.

Motor: Totally enclosed air over (TEAO) cooled motor with sealed lifetime pre-lubricated ball bearings, motor starter and thermal overload protection.

SPECIFIER NOTE – Select one of the following paragraphs and delete the one not required.

LPN2 Units: Wired for single speed operation.

LPV2 Units: Wired for variable speed operation.

SPECIFIER NOTE – Select one of the following paragraphs and delete the one not required. Note that Electrical Characteristics below do not include electric heater requirements. Note that all motors listed are based on 60 Hz service. For units wider than 84 inches, refer to submittal for total amps. For other voltages, contact manufacturer.

Electrical Characteristics: 115V AC, single phase; 2.4 Amp (units up to 48 inches wide) or 2.6 Amp (units 60 to 72 inches wide) full load per motor/fan.

Electrical Characteristics: 208/230V AC, single phase; 1.2 Amp (units up to 48 inches wide) 1.4 Amp (units 60 to 70 inches wide) full load per motor/fan.

Meets NEC. ETL Listed to conform to UL 507 (US) and CSA22.2 (Canada) Standards.

Fans: Tangential type, double width, directly driven by an electric motor.

Provide resilient isolation dampening mountings between motor frame and housing.

Factory balanced blower wheel assembly statically and dynamically.

Housing: Self-contained one-piece type for units up to 72 inches in length with sufficient strength for mounting from pre-punched mounting holes at both ends to ceiling without intermediate support. Units longer than 72” are two units tandem mounted next to each other.

Size:

SPECIFIER NOTE – Select one of the following paragraphs and delete the ones not required. Heated units are mounted inside only; coordinate with heating paragraphs if required.

Unheated: 8-7/8 inches deep by 8 inches high (including discharge nozzle) by width of unit.

Electric Heated: 11-3/4 inches deep by 8 inches high (including discharge nozzle) by width of unit.

Hot Water/Steam Heated: Depth 11-3/4 inches by 8 inches high including discharge nozzle by width of unit plus 10 inches for manifolds

Mounting:

SPECIFIER NOTE – Select one of the following paragraphs and delete the ones not required. Heated units are mounted inside only; coordinate with heating paragraphs if required.

Unheated Inside Mount.

Heated Inside Mount.

Unheated Outside Mount.

Mount Location Indicated.

Material:

SPECIFIER NOTE – Select one of the following two paragraphs and delete the one not required.

Provide 18- and 20-gauge electro or hot dipped galvanized steel sheet housing conforming to ASTM A 591 and/or ASTM A 653.

Provide type 304 stainless steel housing with brushed finish. ASTM A 240/A 240M.

Air Inlet Grille and Filters:

Location: Front.

SPECIFIER NOTE – Select one of the following air inlet type paragraphs and delete the ones not required.

Type: Fixed air intake grille.

SPECIFIER NOTE – Include the following optional filter paragraph if required and delete if not required.

Filter: Aluminum mesh, 1/4 inch (6.4 mm), washable.

Type: UV Only as follows

UV: UVC & UVV germicidal and odor elimination, 4” UV section with disposable UV bulbs

Discharge: Provide integral discharge nozzle specified.

SPECIFIER NOTE – Select following paragraph for sheet steel housings only. Delete entirely for stainless steel housing. Select color required for steel housing and delete the ones not required. Obsidian Black is standard.

Finish and Color: Provide with, no VOC, corrosion resistant polyurethane powder coated finish for sheet metal housings.

Obsidian Black.

Pearl White.

Titanium Silver.

Stainless Steel.

Environmental Air Curtains: Models for Heights up to 8 feet (2438 mm) for Environmental Separation and Temperature Control and up to 7 feet (2133 mm) for Flying Insect Control.

Discharge Nozzle: Adjustable air foil vanes with a plus/minus 40-degree sweep front to back.

Air Velocity at Nozzle:

SPECIFIER NOTE – Select one of the following paragraphs for the model required and delete the ones not required. If more than one type is required show the location of each type on the Drawings or on the Schedule at the end of this Section.

LPV225-1: 25 Inch (635 mm) Wide Units: 1800 feet/min (9.1 m/s) single 1/6HP motor/fan assembly.

LPV236-1: 36 Inch (915 mm) Wide Units: 1800 feet/min (9.1 m/s) single 1/6HP motor/fan assembly.

LPV242-1: 42 Inch (1067 mm) Wide Units: 1800 feet/min (9.1 m/s) single 1/6HP motor/fan assembly.

LPV248-1: 48 Inch (1220 mm) Wide Units: 1800 feet/min (9.1 m/s) single 1/6HP motor/fan assembly.

LPV260-1: 60 Inch (1524 mm) Wide Units: 1800 feet/min (9.1 m/s) single 1/6HP motor/fan assembly.

LPV272-1: 72 Inch (1830 mm) Wide Units: 1800 feet/min (9.1 m/s) single 1/6HP motor/fan assembly.

LPV284-2: 86 Inch (2184 mm) Wide Units: 1800 feet/min (9.1 m/s) two 1/6HP motor/fan assembly.

LPV296-2: 98 Inch (2489 mm) Wide Units: 1800 feet/min (9.1 m/s) two 1/6HP motor/fan assembly.

LPV2108-2: 110 Inch (2794 mm) Wide Units: 1800 feet/min (9.1 m/s) two 1/6HP motor/fan assembly.

LPV2120-2: 122 Inch (3099 mm) Wide Units: 1800 feet/min (9.1 m/s) two 1/6HP motor/fan assembly.

LPV2144-2: 146 Inch (3708 mm) Wide Units: 1800 feet/min (9.1 m/s) two 1/6HP motor/fan assembly.

Air Speed at Floor: Minimum of 400 fpm (2 m/s) at 1 foot (304 mm) from the floor.

Air Inlet Grille and Filters:

Location: Front.

SPECIFIER NOTE – Select one of the following air inlet type paragraphs and delete the ones not required.

Type: Fixed air intake grille.

SPECIFIER NOTE – Include the following optional filter paragraph if required and delete if not required.

Filter: Aluminum mesh, 1/4 inch (6.4 mm), washable.

Speed: 625 cu ft/min (295 L/s), minimum, per motor/fan assembly.

Sound Pressure Level At 10 feet (3 m) From Nozzle:

SPECIFIER NOTE – Select one of the following paragraphs and delete the ones not required. Coordinate selection with the Model specified above.

Single Motor/Fan Units (LPV2 25-LPV2 36): 49 dBA.

Single Motor/Fan Units (LPV2 42): 50 dBA.

Single Motor/Fan Units (LPV2 48): 52 dBA.

Single Motor/Fan Units (LPV2 60-LPV2 72): 53 dBA.

Two Motor/Fan Units (LPV2 84-LPV2 96): 53 dBA.

Two Motor/Fan Units (LPV2 108-LPV2 144): 54 dBA.

Insect Control Air Curtains: Models for Concession Stand Heights to 4 feet (1219 mm) or Customer Entry Heights to 7 feet (2134 mm) certified to NSF/ANSI Standard 37.

Discharge Nozzle: Wedge-shaped discharge outlet nozzle with adjustable air foil vanes with a plus/minus 40-degree sweep front to back.

Air Velocity at Nozzle:

SPECIFIER NOTE – Select one of the following paragraphs for the model required and delete the ones not required. If more than one type is required show the location of each type on the Drawings or on the Schedule at the end of this Section.

LPN225-1: 25 Inch (635 mm) Wide Units: 1800 feet/min (9.1 m/s) single 1/6HP motor/fan assembly.

LPN236-1: 36 Inch (915 mm) Wide Units: 1800 feet/min (9.1 m/s) single 1/6HP motor/fan assembly.

LPN242-1: 42 Inch (1065 mm) Wide Units: 1800 feet/min (9.1 m/s) single 1/6HP motor/fan assembly.

LPN248-1: 48 Inch (1220 mm) Wide Units: 1800 feet/min (9.1 m/s) single 1/6HP motor/fan assembly.

LPN260-1: 60 Inch (1524 mm) Wide Units: 1800 feet/min (9.1 m/s) single 1/6HP motor/fan assembly.

LPN272-1: 72 Inch (1830 mm) Wide Units: 1800 feet/min (9.1 m/s) single 1/6HP motor/fan assembly.

LPN284-2: 86 Inch (2184 mm) Wide Units: 1800 feet/min (9.1 m/s) two 1/6HP motor/fan assembly.

LPN296-2: 98 Inch (2489 mm) Wide Units: 1800 feet/min (9.1 m/s) two 1/6HP motor/fan assembly.

LPN2108-2: 110 Inch (2794 mm) Wide Units: 1800 feet/min (9.1 m/s) two 1/6HP motor/fan assembly.

LPN2120-2: 122 Inch (3099 mm) Wide Units: 1800 feet/min (9.1 m/s) two 1/6HP motor/fan assembly.

LPN2144-2: 146 Inch (3708 mm) Wide Units: 1800 feet/min (9.1 m/s) two 1/6HP motor/fan assembly.

Air Speed at Floor:

Concession stand windows require a minimum of 600 fpm (3.05 m/s) at 16 inches (406.4 mm) from countertop with Aluminum mesh, 1/4 inch (6.4 mm), washable.

Customer entry doors require a minimum of 600 fpm (3.05 m/s) at 3 feet (914 mm) from floor.

Air Inlet Grille and Filters:

Location: Front.

Speed: 625 cu ft/min (295 L/s), minimum, per motor/fan assembly.

SPECIFIER NOTE – Select one of the following paragraphs and delete the one not required.

Type: Fixed air intake grille.

Type: Aluminum mesh, 1/4 inch (6.4 mm), washable filter.

Sound Pressure Level At 10 feet (3 m) From Nozzle:

SPECIFIER NOTE – Select one of the following paragraphs and delete the ones not required. Coordinate selection with the Model specified above.

Single Motor/Fan Units (LPV2 25 to LPV2 36): 49 dBA.

Single Motor/Fan Units (LPV2 42): 50 dBA.

Single Motor/Fan Units (LPV2 48): 52 dBA.

Single Motor/Fan Units (LPV2 60 and LPV2 72): 53 dBA.

Two Motor/Fan Units (LPV2 84 and LPV2 96): 53 dBA.

Two Motor/Fan Units (LPV2 108 to LPV2 144): 54 dBA.

SPECIFIER NOTE – Select the optional components required from the following paragraphs for the air curtains specified. If more than one type of air curtain or component is required, indicate the location of each curtain and the components required for each location on the Drawings or on the Schedule at the end of this Section. Contact Mars Air Systems for specialty steam and hot water heaters other than those included in the specification.

COMPONENTS

Electric Heaters: Provide complete with motor control panel factory mounted to air curtain housing, and thermostat to be field installed.

Temperature limit controller.

SPECIFIER NOTE – Thermostat is standard. Coordinate selection with Model specified above. Delete if not required.

Thermostat: Wall-mounted, 115-Volt operation, with heater on/off selection.

Thermostat: Wall-mounted, 208-Volt operation, with heater on/off selection.

Thermostat: Wall-mounted, 230-Volt operation, with heater on/off selection

Thermostat: Wall-mounted, 24-Volt operation, with heater on/off selection.

Heating Coils: ETL approved as part of unit. CEC tested by ETL. Factory mounted on the discharge end of the motor fan assembly and located within the nozzle outlet.

Steam Heaters: Provide finned tube steam coils for field mounting on air intake side of the air curtain cabinet with opposite end connections.

Meets NEC and CEC tested by ETL Certified to conform to UL1995(US) and CSA22.2 (Canada) Standards.

Output: Air curtain manufacturer's standard, one-row coils.

Coils: Certified in accordance with AHRI 410.

SPECIFIER NOTE – Delete two of the following three connections paragraphs.

Connections: Same end, right hand, horizontal.

Connections: Same end, left hand, horizontal.

Casing: One-piece unpainted galvanized steel, bolted to air curtain housing

Supply and return fittings on ends of casing.

SPECIFIER NOTE – Thermostat is standard. Coordinate selection with Model specified above. Delete if not required.

Thermostat: Wall-mounted 115-Volt operation, with heater on/off selection.

Thermostat: Wall-mounted 208-Volt operation, with heater on/off selection.

Thermostat: Wall-mounted 230-Volt operation, with heater on/off selection.

Thermostat: Wall-mounted optional 24-Volt operation, with heater on/off selection.

Hot Water Heaters: Provide finned tube water coils for field mounting on air intake side of the air curtain cabinet with opposite end connections.

Meets NEC and CEC tested by ETL Certified to conform to UL1995(US) and CSA22.2 (Canada) Standards.

Output: Air curtain manufacturer's standard, one-row coils.

Coils: Certified in accordance with AHRI 410.

SPECIFIER NOTE – Delete two of the following two connections paragraphs.

Connections: Same end, right hand, horizontal.

Connections: Same end, left hand, horizontal.

Casing: One-piece unpainted galvanized steel, bolted to air curtain housing.

Supply and return fittings on ends of casing.

SPECIFIER NOTE – Thermostat is standard. Coordinate selection with Model specified above. Delete if not required.

Thermostat: Wall-mounted 115-Volt operation, with heater on/off selection.

Thermostat: Wall-mounted 208-Volt operation, with heater on/off selection.

Thermostat: Wall-mounted 230-Volt operation, with heater on/off selection.

Thermostat: Wall-mounted optional 24-Volt operation, with heater on/off selection.

Door-Activated Limit switch(s): Provide, field installed 250-Volts, 20 amps limit switch to control air curtain(s) as follows; Automatic on/off control, activates air curtain when door is opened and turns off when door is closed. Provide limit switch for direct control one 1 HP or up to two 1/2 HP single phase motors without a separate control panel. Provide a separate control panel for three-phase motors and/or units exceeding 1 HP, 250-Volts or 20 amps controlled by a limit switch.

SPECIFIER NOTE – Select the Type required from the following two paragraphs.

Type: Combination plunger/roller switch for swing and sliding doors.

SPECIFIER NOTE – Select one of the following paragraphs to suit enclosures for incidental contact, protection against weather and corrosive exposure and explosion proof as required.

Provide limit switches with NEMA 1 (20 amps) ratings in locations indicated.

Provide limit switches with NEMA 4X (10 amps) ratings in locations indicated.

Provide limit switches with NEMA 7 (10 amps) ratings in locations indicated.

Type: Magnetic reed switch and actuator for swing and sliding doors. Industrial floor mounted or surface mounted switches for roll up doors

SPECIFIER NOTE – Edit the following paragraphs to suit the units specified. Delete the paragraph not applicable if it is not required.

Operation for Unheated Units: Automatic on/off control, on when door is opened, off when door is closed.

Operation for Heated Units: Automatic on when door is opened, off after time delay period after door is closed, maintaining heat in the event door is opened within time delay period. Field adjustable from 1 to 17 minutes.

SPECIFIER NOTE – Select the following optional controller if required. Delete if not required.

Optional Digital Programmable Controller:

WiFi enabled controller for wireless interface with field supplied smartphone, tablet or computer

No download or app required for wireless interface

Wireless control range up to minimum of 50 feet from controller

Fully factory assembled and wired inside the air curtain for easy field installation

Optional remote mounted high resolution 7” Color LCD Display with resistive touchscreen technology

Fully programmable controller

Connect and control via any web browser

Factory built wireless router with over 50 feet range

Pre-set and fully customizable programs

Time delay (Passive & Adaptive)

Factory Integrated temperature control sensors. No external thermostat required.

Heat on Demand Mode to regulate the space temperature

Summer-Winter modes

24/7/365 timer

Maintenance schedule alerts

Password protected

High temperature lock from fan failure

Low voltage control signal for door activation

Multispeed fan control

Optional Integrated BMS controls

Optional BACnet MS/TP

Optional BACnet IP

Optional adaptive fan speed control and heat control based on existing field conditions. Field mounted outdoor temperature sensors required.

Provide mounting hardware as required for the opening.

EXECUTION

EXAMINATION

Verify that required utilities are in correct location and are of correct capacities for specified products.

Verify openings to receive air curtains are plumb, level, square, accurately aligned, correctly located, and in tolerance.

Examine surfaces to receive air curtains. If surface preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

INSTALLATION

SPECIFIER NOTE – Indicate the mounting location(s) on the Drawing or on the Schedule at the end of this Section. Units are typically wall mounted horizontally above the door opening. Units can also be suspension mounted from the ceiling or vertically mounted alongside the opening. Heated units must be mounted on the inside or protected side of the opening.

Install air curtains in accordance with approved shop drawings and manufacturer's printed installation instructions.

Install air curtains plumb, level, square, true to line, and weathertight, without warp or rack.

Anchor air curtains securely in place to supports.

Coordinate with sheet metal flashing as specified in Section 07 62 00.

Install joint sealants as specified in Section 07 92 00.

Coordinate with electrical power as specified in Section 26 05 00.

Install door limit switches and adjust for correct operation.

Provide connection to piped services and utilities as specified in Section 22 10 00 and 23 21 00.

FIELD QUALITY CONTROL

Adjust air curtains to function properly.

Adjust air foil vanes located within the discharge nozzle as required for prevailing conditions at each opening.

Check heated air curtain performance on a calm day by measuring air temperature 6 inches off the floor. Optimal reading is halfway between the temperature inside and outside the building.

CLEANING

Clean air curtains promptly after installation in accordance with manufacturer's instructions.

Repair minor damages to finish in accordance with manufacturer's instructions and as approved by Architect.

Remove and replace damaged components that cannot be successfully repaired as determined by Architect.

PROTECTION

Protect materials and finish from damage until substantial completion.

SPECIFIER NOTE – For facilities with multiple types and sizes of air curtains use an Air Curtain Schedule to list requirements for each size, type, HP, and power requirements of air curtain(s) required. Delete if not required.

SCHEDULES

Refer to Air Curtain Schedule appended to this section.

END OF SECTION